# Name: _____________________________________________ Date: ______________ Period: _______

# General Science

# Free-Body Diagrams

# Features of free-body diagrams

- Free-body diagrams are vector diagrams used to show the magnitude and direction of forces acting on an object in a given situation.

- The size of the arrow in a free-body diagram represents the magnitude of the force. The arrow’s direction shows the direction that the force acts.

- Each force arrow is labeled to indicate the type of force.

- A box represents the object that the forces are acting upon. Force arrows are drawn from the center of the box outward in the direction in which each force acts.

# Typical Forces to Account for in Mechanics Problems

- Fapp: Applied force. This is a force applied to an object, usually by a person or an engine.

- Fg: Force due to gravity; also known as weight. All objects on Earth experience this force, which is directed to the Earth’s center. On most free-body diagrams, this force is directed downwards. Sometimes the symbol W is used in place of Fg.

- Fn: Normal force. This is the support force exerted on an object in contact with another stable object, like a floor or tabletop. This force is draw perpendicularly to the surfaces in contact. Sometimes the symbol n is used in place of Fn.

- Ff: Friction force. This force is exerted by a surface on an object and opposes the motion of the object. Sometimes the symbol f is used in place of Ff.

- Fair: Air resistance. This force is exerted by the air on moving objects and opposes the motion of the object.

- Ft: Tension. Tension is a force transmitted through supports such as strings or wires. It is directed along the strings. Sometimes the symbol T is used in place of Ft.

# Free Body Diagrams and Force Equilibrium

- A pencil rests on a desk.

- You push a book across your table from right to left at constant velocity.

- A girl sits motionless on a tree swing which has two ropes connected to a tree branch.

- A skydiver coast down to the ground with constant velocity.

# Free Body Diagrams and Acceleration

- A block is pushed from right to left and it is increasing in speed.

- A rock is dropped from the top of a ladder and no air resistance acts on it.

- A hockey puck slowly slides to rest as it moves right to left.